## Slide 1: Course name: Electrical & Electronics System (EE1002)
Course code : EE 1002
lecture series no : 10 (ten)
Credits : 04
Mode of delivery : oFF line (Power point presentation)
Faculty : Mr. ritesh singh
Email-id : ritesh.singh@jaipur.manipal.edu
PROPOSED DATE OF DELIVERY: 16 Aug 2023
B.TECH FIRST YEAR
ACADemic YEAR: 2023-2024

## Slide 2: Session outcome
“Analyse DC circuit using Thevenin’s theorem & Maximum Power Transfer Theorem”

## Slide 3: Assessment criteria’S
Assignment
quiz
mid term examination
END TERM EXAMINATION

## Slide 4: PROGRAM OUTCOMES MAPPING WITH CO1
[PO1]
Engineering Knowledge: Apply the knowledge of mathematics, science, engineering fundamentals, and an engineering specialization to the solution of complex engineering problems.

## Slide 5
DC Network Theorems:
Thevenin’s Theorem and Maximum Power Transfer Theorem
Lecture No. 11

## Slide 6
Contents
Topic:
1. Thevenin’s Theorem
2. Maximum Power Transfer Theorem

## Slide 7
Thevenin’s Theorem
Steps to Analyze an Electric Circuit
Open the load resistor.
Calculate / measure the open circuit voltage. This is the Thevenin Voltage (VTH).
Open current sources and short voltage sources.
Calculate /measure the Open Circuit Resistance. This is the Thevenin Resistance (RTH).
Now, redraw the circuit with measured open circuit Voltage (VTH) in Step (2) as voltage source and measured open circuit resistance (RTH) in step (4) as a series resistance and connect the load resistor which we had removed in Step (1). This is the equivalent Thevenin circuit of that linear electric network or complex circuit which had to be simplified and analyzed by Thevenin’s Theorem. You have done.
Now find the Total current flowing through load resistor by using the Ohm’s Law: IT = VTH / (RTH + RL).

## Slide 8
Problem-1: Find VX by first finding VTH and RTH to the left of A-B using Thevenin Theorem.
THEVENIN TEOREM
Step-1 Open the load resistor.
Step-2 Calculate the open circuit voltage. This is the Thevenin Voltage (VTH).

## Slide 9
Notice that there is no current flowing in the 4  resistor (A-B) is open. Thus there can be no voltage across the resistor.
We now deactivate the sources to the left of A-B and find the resistance seen looking in these terminals as shown in Fig.
Step-3 & 4 Open current sources and short voltage sources and calculate the Open Circuit Resistance.
This is the Thevenin Resistance (RTH).

## Slide 10
RTH = 12||6 + 4 = 8 
RTH
Step-5 Now draw the equivalent Thevenin circuit of that linear electric network or complex circuit which had to be simplified and analyzed by Thevenin’s Theorem.

## Slide 11
We connect this to the load in order to find VX.

## Slide 12
We first find VTH with the 17  resistor removed. Next we find RTH by looking into terminals A-B
with the sources deactivated.
Problem-2: In the circuit given circuit, find VAB by using Thevenin Theorem.
Step-1 Open the load resistor.
Step-2 Calculate the open circuit voltage. This is the Thevenin Voltage (VTH).

## Slide 14
To calculate the value of the thevenin resistance all sources are changed to their internal resistance like voltage source is changed to short circuit and the current source is changed to open terminal. In addition for calculating the value of RTH this circuit is viewed from the open terminal.
RTH

## Slide 15
Now we can see that,
VAB = VTH *17/(14+17)

## Slide 16
Maximum Power Transfer Theorem
This theorem states that the output obtained from a network is maximum when the load resistance RL is equal to the internal resistance of the network as seen from the terminals of the load.
According to Thevenin theorem, every network can be represented by a single voltage source (Thevenin source) having an effective internal resistance Rth as shown in Figure.
Let us determine the value of load resistor RL so that source delivers maximum power to it.

## Slide 18
Thus, for maximum power transfer, the load resistance RL must be made equal to the internal resistance of the source (or of the whole network) Rth.
In this case, the efficiency will by very poor only 50%, but the low efficiency is of no importance because the aim is to transfer the maximum power at the output. Now the maximum power transfer to the load of the circuit is given by:

## Slide 19
Problem-1: Find the value of load resistance RL for maximum power flow through it in the circuit shown in
Figure1.
The power drawn by the load resistor RL will be maximum when its value is equal to the Thevenin equivalent resistance of the network. To determine Rth across terminal AB (load), remove RL and replace the sources by their internal resistances, that is, short circuit the voltage source and open circuit the current source, as shown in Figure 2.
Fig 1
Fig 2
Rth = 2.43Ω
The power transferred to the load by the source will be maximum when:
RL = Rth = 2.43Ω

## Slide 20
Problem-2: Determine the value of load resistance RL to give maximum power transfer and the power delivered to the load as shown in Figure1.
The equivalent resistance of the network when viewed from terminals A and B after removing resistor RL from the circuit and short circuiting the voltage source.
Fig 1
Fig 2
We get Thevenin resistance

## Slide 21
Maximum power will be transferred to the load, when it is equal to Thevenin’s equivalent resistance Rth,
RL = Rth = 9 Ω
When the terminals A and B are open (i.e., load resistor RL is removed), the current flowing
through the mesh ECDFE, as shown in Figure.
Open-circuit voltage across AB, VAB = VCD = Eth = 10 × 1 = 10 V
Maximum power delivered to the load,

## Slide 22
THANK YOU