## Slide 1: Course name: Electrical & Electronics System (EE1002)
Course code : EE 1002
lecture series no : 01 (one)
Credits : 04
Mode of delivery : oFF line (Power point presentation)
Faculty : Himanshu PRIYADARSHI
Email-id : Himanshu.priyadarshil@jaipur.manipal.edu
PROPOSED DATE OF DELIVERY: 16 Sept 2023
B.TECH FIRST YEAR
ACADemic YEAR: 2023-2024

## Slide 2: Session outcome
“Describe the phasor operations and calculation of different quantities pertaining to different combinations of series ac circuits”

## Slide 3: Assessment criteria’S
Assignment,
Quiz, Mid terms and End term.

## Slide 4: CO2 mapped with PROGRAM OUTCOMES MAPPING WITH [po1],[po2], & [po12]

## Slide 5: Dept. of Electrical & Electronics Engineering School of Electrical, Electronics & Communication SEEC Faculty of Engineering
Single Phase Circuits
Phasors, Analysis of pure R, L, C, Series RL, RC & RLC circuits, Impedance, Power, Power factor

## Slide 6
Contents
Single phase circuits:
1. Phasors
2. ‘j’ operator

## Slide 7: 1. Introduction to Phasors
v(wt) = Vm sin wt
v() = Vm sin 
w
a
a
wt
v
Vm
0
p
2p
Vm
Vm
-Vm
0
N
S
a
b
Coil
Rotation
A phasor is a graphical representation of the magnitude and angular position of a time varying quantity such as a voltage or current in which variation is sinusoidal.
A phasor diagram can be used to show the relative relationship of two or more sine waves of the same frequency.

## Slide 8
Leading Sine Wave
wt
Vm
Im

i(ωt)
v(ωt)

Phase angle is the angular difference between the two quantities under consideration.
One quantity is the reference
Im leads Vm (or i leads v) by an angle  where Vm is the reference.
Time domain: v(t) = Vm sin(ωt); i(t) = Im sin (ωt + )
Polar form: V = Vm / 0o; I = Im /

## Slide 9
Lagging Sine Wave
v(ωt)
wt
Vm
Im

i(ωt)

0
Im lags Vm (or i lags v) by an angle 
Time domain: v(t) = Vm sin(ωt); i(t) = Im sin (ωt - )
Polar form: V = Vm / 0o; I = Im /-

## Slide 10
The ‘j’ operator
A
jA
O
Any phasor when operated by ‘j’ is rotated in anticlockwise direction by 90 degrees.
jOA = OA /90 ;
j*jOA = - OA = OA /180 ;

## Slide 11
The ‘j’ operator …

x
A
B
C
O
y
A phasor can be resolved into two components at right angles to each other.
  OA is a phasor.
  Horizontal component = OB
  Vertical component OC = AB
  OA=OB + jOC

## Slide 12: Phasor Representation
Two forms of representation:
Polar form: represented by magnitude and the angle
Rectangular form: represented by its X and Y coordinates

0

2
Im
A
θ1
θ2
B
IA
IB
i
θ1
θ2
X - Ref.
y
A
B

## Slide 13
Exercise
Convert the following into polar form using calculators
Convert the following into rectangular form using calculators

## Slide 14
  Pure resistive circuits
  Pure inductive circuits
  Pure capacitive circuits

## Slide 15
1. Pure resistive circuits
2
t
v(t)
0
/2

i(t)
i(t)
v(t)
R
Let
v(t) = Vm sin t --------------- (1)
= Im sin t -------------(2)
Where I = Irms
Phasor diagram
Phase angle between V & I = 0
current through the resistor is in phase with the voltage across it.
V & I are RMS values

## Slide 16
Pure Resistive Circuits - Power Consumed
Instantaneous power,
  p(t) = v(t).i(t)
  = Vm Im sin2t
2
t
p(t)
v(t)
0
/2

i(t)

## Slide 17
2. Pure Inductive Circuits
v(t)
L
+
-
e(t)
i(t)
t
/2

3/2
2
v(t)
i(t)

## Slide 18
Pure Inductive Circuits - Phasor diagram
Current through pure inductor lags the voltage across it by .
  Vm = L Im.
  = XL Im.
  XL = L = 2f L ----- inductive reactance, in ohm
  Phasor Diagram
90º
Phase difference = 90º

## Slide 19
Pure Inductive Circuits …
The inductive reactance is directly proportional to frequency.
  XL = L = 2f L
The current through pure inductor is inversely proportional to frequency.
  I = V/(L)
Frequency
0
Inductive
reactance
Current

## Slide 20
Pure Inductive Circuits -Power Consumed
Instantaneous power,
  p(t) = v(t).i(t)
  = Vm Im sint. sin(t-90)
  = - Vm Im cost. sint
= -(Vm Im/2) sin2t
Average Power Consumed in a Pure Inductor
The net (average/active) power absorbed in a pure Inductor is zero
t
/2

3/2
2
v
i
p
0

## Slide 21
3. Pure Capacitive Circuits
i(t)
v(t)
C
2
i(t)
t
/2

3/2
v(t)

## Slide 22
Pure Capacitive circuits - Phasor diagram
Current through pure Capacitor leads the voltage across it by 90º.
  Vm = Im/(C)
  = XC Im.
  XC = 1/(C) = 1/(2f C) -----
  Capacitive reactance, in ohm
  Phasor Diagram
90º
Phasor diagram
Phase difference = 90º

## Slide 23
Pure Capacitive Circuits…
The capacitive reactance is inversely proportional to frequency.
  XC = 1/ ( C)
The current through a pure capacitor is directly proportional to frequency.
  I =  C V
Frequency,
0
Capacitor current
Capacitive Reactance

## Slide 24
Pure Capacitive Circuits - Power Consumed
Instantaneous power,
  p(t) = v(t).i(t)
  = Vm Im sint. sin(t+90)
  = Vm Im cost. sint
= (Vm Im/2) sin2t
Average Power Consumed in a Pure Capacitor
t
/2

3/2
2
v
i
p
0
The average/active power consumed by a pure Capacitor is zero.

## Slide 25
  Series RL Circuits
  Series RC Circuits
  Illustrations

## Slide 26
1. Series RL Circuit
Phasor Diagram -
90º

Reference
(phasor)
R
L
v(t)
i(t)

## Slide 27
Series RL Circuit - Complex Impedance
The phase difference between V & I is termed as phase angle , .
Also  is termed as Impedance angle
Complex Impedance
90º

Reference
(phasor)
90º

Reference
(phasor)

## Slide 28
Series RL Circuit - Waveforms
The current lags behind the voltage by a phase angle 
t
/2

3/2
2
v
i


## Slide 29
2. Series RC Circuit – Phasor diagram
R
C
v(t)
i(t)
-90º

Reference
(phasor)
Phasor Diagram -

## Slide 30
Series RC Circuit - Complex Impedance
Complex Impedance
The phase difference between V & I is termed as phase angle , .
 is the Impedance angle
-90º

Reference
(phasor)
-90º

Reference
(phasor)

## Slide 31
Series RC Circuit - Wave forms
The current Leads behind the voltage by a phase angle 
t
/2

3/2
2
v
i


## Slide 32
Solved Examples
  A resistance of 50 is connected in series with an inductance of 100 mH across a 230V, 50 Hz, single phase AC supply. Calculate
  a) impedance
b) current drawn
c) power factor
d) power consumed
e) Draw the phasor diagram.

## Slide 33
  Ans.
a) Z =
b) I =
c) Pf =
d) P = 759.15W
0.847 lag
I
VR
VL
V
32.12º
e)

## Slide 34
  2. A resistance of 50 is connected in series with a capacitance
  of 100 F across a 230V, 50 Hz, single phase AC supply.
  Calculate
  a) impedance
b) current drawn
c) power factor
d) power consumed
e) Draw the phasor diagram.

## Slide 35
  Ans.
a) Z =
b) I =
c) Pf =
d) P = 752.81W
0.847 lag
0.843 lead
e)
I
VR
VC
V
32.48º

## Slide 36
  Series RLC Circuits
  Complex power
  Illustrations

## Slide 37
Series RLC Circuit
Let i(t) = Im sint
Impedance, Z=R+j(XL-XC)
(i) If XL=XC , resistive circuit
(ii) If XL>XC, RL series circuit
(iii) If XL<XC, RC series circuit
L
v(t)
i(t)
R
C
Note: - i(t) is the reference

## Slide 38
Series RLC Circuit
L
v(t)
i(t)
R
C

## Slide 39
Series RLC Circuit – Power consumed
Instantaneous power
Average power
            = Active Power
Cos  is called the power factor

## Slide 40
Power Triangle
P = Average power = Active power =
measured in Watt
Q = Reactive power =
measured in VAr
(Volt-Amp reactive)
S = Absolute power = Apparent power =
measured in VA (Volt-Amp)
90º

90º


## Slide 41
Complex Power
For inductive loads, current is lagging, the angle  is negative.
Q = Reactive power =
But in SI units, lagging reactive power is +ve.
Hence, conjugate of the angle  is used in power calculations.
S = VI* = = =
S = P + j Q
Similarly For capacitive loads, reactive power is –ve in SI units.
S = VI* = = =
S = P - j Q

## Slide 42
Power Factor
- Ratio of active power to absolute power
- Also, cosine of the impedance angle is numerically same as power factor.

## Slide 43
Solved Examples
1. The value of the capacitor in the circuit given below is 20 F and the current flowing through the circuit is 0.345 A. If the voltages are as indicated, find the applied voltage, the frequency and loss in the coil.
C
R
L
RL
I
V
25 V
40 V
55 V
coil
50 V

## Slide 44
Power Loss = 1.8967 W

## Slide 45
  2. A resistance of 50 is connected in series with an inductance of 100 mH across a 230V, 50 Hz, single phase AC supply. Calculate
  a) impedance
b) current drawn
c) power factor
d) power consumed
e) Draw the phasor diagram.

## Slide 46
a) Z =
b) I=
c) Pf =
0.847 lag
d) P = 759.15W
I
VR
VL
V
32.12º
e)
Ans:

## Slide 47
  3. A resistance of 50 is connected in series with a capacitance of 100 F across a 230V, 50 Hz, single phase AC supply. Calculate
  a) impedance
b) current drawn
c) power factor
d) power consumed
e) Draw the phasor diagram.

## Slide 48
a) Z =
b) I =
c) Pf =
0.843 lag
d) P = 752.81W
Ans:
e)
I
VR
VC
V
32.48º

## Slide 49
4. Write the nodal equations for the network shown in Figure and express them in matrix form.