## Slide 1: Course name: Electrical & Electronics System (EE1002)
Course code : EE 1002
lecture series no : 01 (one)
Credits : 04
Mode of delivery : oFF line (Power point presentation)
Faculty : HIMANSHU PRIYADARSHI
Email-id : Himanshu.priyadarshi@jaipur.manipal.edu
PROPOSED DATE OF DELIVERY: 16 Aug 2023
B.TECH FIRST YEAR
ACADemic YEAR: 2023-2024

## Slide 2: Session outcome
“Analyse and calculate different quantities pertaining to parallel ac circuits”

## Slide 3: Assessment criteria’S
Assignment,
Quiz, Mid terms and End term.

## Slide 4: CO2 mapped with PROGRAM OUTCOMES MAPPING WITH [po1],[po2], & [po12]

## Slide 5: Dept. of Electrical & Electronics Engineering School of Electrical, Electronics & Communication SEEC Faculty of Engineering
Single Phase Circuits
Series & Parallel Resonance, Resonant frequency, Voltage & Current magnification, Dynamic resistance
Lecture 13 - 15

## Slide 6
Contents
Single Phase Circuits:
1. Series Resonance
2. Parallel Resonance
Resonant frequency
Voltage & Current magnification
Dynamic resistance

## Slide 7
Series Resonance
Reference books :
Chapter 13 of Hughes E, Electrical and Electronic Technology (8th e), Pearson Education, 2002.
Chapter 4(4.14) of T.K.Nagsarkar & M.S.Sukhija, Basic Electrical Engineering, OXFORD University Press.

## Slide 8
SERIES RESONANCE - RLC Series Circuit
v(t), variable frequency
  Is said to be in resonance, when
    Current is in phase with voltage
      Inductive reactance =Capacitive reactance; XL = XC
      Circuit Power factor is unity
      Effective Circuit impedance is resistive; Z = R

## Slide 9
SERIES RESONANCE - Resonant frequency (f0)
v(t), variable frequency
At series Resonance
  Resonant frequency (f0)

## Slide 10
Variation of Reactance with frequency
XL=ωL
XC=-1/ωC
ω
o
R
XL=ωL
XC=-1/ωC
ω
o
R
XL=ωL
XC=-1/ωC
ω
o
R
XL=ωL
XC=-1/ωC
ω
o
R
XL=ωL
XC=-1/ωC
ω
o
R
ωo
ω0 is the resonance frequency.
  Series Resonance

## Slide 11
SERIES RESONANCE - Variation of Current
ωo
ω
I
I0
Acceptor circuit
at resonance Irms is maximum when XL = XC;

## Slide 12
SERIES RESONANCE - Variation of phase angle
ω
ωo
o
For -
  ω< ωo; XC>XL leading current
  ω= ωo; XC=XL in phase current
  ω> ωo; XC<XL lagging current

## Slide 13
Series Resonance - Bandwidth and Half Power frequencies
ω1
ωo
ω2
i
IO
ω
= Half the power at
resonant frequency
ω1 = lower half power frequency
ω2 = upper half power frequency
Band Width = ω2- ω1

## Slide 14
Relation between Band Width and Half Power Frequencies

## Slide 15
Series Resonance - Q - Factor
Quality factor- a measure of selectivity

## Slide 16
SERIES RESONANCE - Voltage Magnification
  At Series Resonance
  Sharpness of resonance depends on R
    Small R gives sharp resonance
    Large R gives broad resonance

## Slide 17
Parallel Resonance

## Slide 18
PARALLEL RESONANCE - Characteristics
At Resonance Voltage and current must be in phase
Hence in the case of Parallel Resonance :
  The admittance of the circuit is minimum at resonance so Z is maximum & I in minimum.
  The current (maximum) drawn from the supply is V/R
  The currents IC and IL are equal and opposite.
  Power factor is unity
  Net susceptance is zero
v(t)
R
L
iR
iC
iL
C

## Slide 19
PARALLEL RESONANCE - Resonant frequency (fr)
For pure RLC parallel circuit
At resonance, the net susceptance is zero for Parallel Resonance.
Same expression as in case of Series resonance
Let  be variable and r = Resonant frequency (fr)
v(t)
R
L
iR
iC
iL
C

## Slide 20
PARALLEL RESONANCE - Resonant frequency (fr)
For the Circuit shown…
At resonance, the net susceptance is zero for Parallel Resonance (C – 1/ L)=0 .
2
1
÷
ø
ö
ç
è
æ
-
=
L
R
LC
r
w
R
L
C
v(t)

## Slide 21
PARALLEL RESONANCE - Current magnification
Φ
Φ
R
ωL
R
L
C
v(t)
I
I
L
I
C
At resonance, IL and IC >>>I
Current magnification,

## Slide 22
PARALLEL RESONANCE - Variation of current
I
ω
ωr
o
At resonance Current is minimum (as its reactive part = 0);
Thus, Maximum Impedance = Dynamic Impedance =
Also called Rejector circuit.

## Slide 23
Defined as the ratio of the line current () , circulating between the two branches of the parallel circuit to the line current.
were,
Thus,
And at resonance,
In series circuit gives Voltage Magnification &
In parallel circuit gives Current Magnification.

## Slide 24
Solved Examples
[1] A series RLC circuit consisting of R=100Ω, L=10mH and C=100μF is supplied by an ac supply of 100 volt at varying frequency.
Determine
  Resonant frequency
  Current at resonance
  Half power frequencies
  Q factor
  Voltage across capacitor

## Slide 25
Sol.

## Slide 26
[2] An RLC series circuit of R=8Ω resistance should be designed to have a bandwidth of 50 Hz. Determine the value of L and C so that the system resonates at 200 Hz.

## Slide 27
[3] The parallel circuit shown in figure is made to resonate by varying L. Find the value of L if ω=5000rad/sec .
Sol.
Z1=5-j10Ω
XL = 12.17 Ω or 0.3286Ω
L = 65.73μH or 2.434mH
Im(Y1+Y2)=Im(Y) =
Z2=2+jXLΩ

## Slide 28
[4] Show that circuit given in figure will be at resonance at supply frequency
Sol.
  Given ω=1.4 rad/sec
  Find overall impedance (admittance)
  If it results in real answer, then frequency at resonance is 1.4 rad/sec